## Slide 1: Welcome to Stavanger/Norway University of Stavanger uis.no
Bente Dale, International Office
ROS2/Gazebo - Marine Simulator v1.1
An international university campus across 1300 acres of land
Professor Yihan Xing
Study program leader, MSc Marine and Offshore

## Slide 2: Updates from MARSIM v1.0
Improved documentation
  Theory behind extended karman filter (EKF)
  References folder
Upgraded marsim_gazebo package
  Updated models
    Added camera and depth camera to models/bluerov2
    Created namespace for models/bluerov2
    worlds/empty.world has now vessel_g in the middle
  New models
    models/sst
    models/vessel_g
Added marsim_control package
  scripts/bluerov2_pid_pose_z_control.py
Added matlab_tools
  Supplementary tools for tuning of controllers, estimation of hydrodynamic coefficients, etc.

## Slide 3: Agenda
Docker Engine
ROS2
Gazebo
Marine Simulator Gazebo (marsim_gazebo) package
Marine Simulator Control (marsim_control) package

## Slide 4: Docker Engine
Open-source containerization tool
Docker container:
  Run-time environment with the applications to be run and their dependencies
Docker image:
  Standalone and executable file that is used to create the container
  Contains all files required (application, libraries, dependencies, etc.)
  Sharable and portable
Source: https://docs.docker.com/guides/docker-overview/#docker-architecture
Source: https://www.docker.com/resources/what-container/

## Slide 5: Docker workflow process
Step 1: Build the Docker image (Dockerfile)
  Use a Dockerfile for easier defintion of the image to be built
Step 2: Load the Docker image as a container (load_dock.sh)
  This is the main terminal of the container. Exiting from this terminal will unload the container.
  No files will be saved in the container upon unloading.
  Load and use a share volume from the host machine for saving work files.
Step 3: Access the running Docker container if more additional terminals are required (access_cont.sh)
Step 4: Exit from the container
  Exiting from the main terminal will unload the container

## Slide 6: DockerFile
Base image
  Example: nvidia/cuda:12.6.1-base-ubuntu24.04
  https://hub.docker.com/r/nvidia/cuda
  Reason: I am using a laptop that has NVIDIA RTX 2000 Ada. The Cuda base image has already many of the required graphics drivers pre-installed and configured.
Install packages
  Sudo not required; the build process runs in root
  Install ROS2 jazzy, Gazebo harmonic, Gazebo/ROS pairing, misc ROS2 tools and misc tools

## Slide 7: Load and run Docker container
load_dock.sh
  xhost +local:docker: Allows the Docker container to access the host's X server for GUI applications.
  Container options: -it: Interactive mode with a pseudo-TTY; --rm: Automatically remove the container when it exits; --privileged: Gives extended privileges to this container; --gpus all: Allows the container to use all available NVIDIA GPUs; --name marsim_sdf_cont: Names the container "marsim_sdf_cont".
  Environment variables: XDG_RUNTIME_DIR=/tmp/runtime-root: Sets the runtime directory; DISPLAY=$DISPLAY: Passes the host's DISPLAY environment to the container; QT_X11_NO_MITSHM=1: Disables MIT-SHM extension for Qt applications: MESA_GL_VERSION_OVERRIDE=3.3: Forces OpenGL version 3.3 for Mesa drivers.
  Volume mounts: /tmp/.X11-unix:/tmp/.X11-unix: Mounts X11 socket for GUI support; /home/yhxing/Docker_WS/marsim1:/home/marsim_ws:rw: Mounts a local directory into the container with read-write access;
  --runtime=nvidia: Specifies to use the NVIDIA Container Runtime.
access_cont.sh
load_dock.sh
access_cont.sh

## Slide 8: Robot Operating System 2 (ROS2)
Material is taken from Rico, F. M. (2022). A concise introduction to robot programming with ROS2. Chapman and Hall/CRC.
ROS2 is not an operating system; it is a middleware developed and maintained by the Open Robotics Foundation
Middleware is a layer of software between the operating system and the user applications
ROS2 is the 2nd generation of ROS
Source: Rico, F. M. (2022). A concise introduction to robot programming with ROS2. Chapman and Hall/CRC

## Slide 9: ROS2 architecture
User nodes interface with ROS2 via RCL’s APIs
rcl is the core of ROS2 and is written in C
rclcpp, rclpy, rclc, etc binds different programming languages to rcl offering the same behaviour, i.e., they are not independent implementations
ROS2 is a distributed system using data distribution system (DDS) as its communications layer
There are several DDS vendors; ROS2 Humble uses Cyclone DDS
Source: Rico, F. M. (2022). A concise introduction to robot programming with ROS2. Chapman and Hall/CRC

## Slide 10: ROS2 vs ROS1
Architecture
  DDS (ROS2) vs Master-Slave Architecture and the XML-RPC middleware (ROS1)
  rcp with binders to any programming language (ROS2) vs two seperate libraries roscpp and rospy (ROS1)
Features
  QoS, multi-threaded exectution and real-time processing
Tooling/Ecosystem
  Not backward compatible, but interface with ROS1 can be done via ROSbridge
Maruyama, Y., Kato, S., & Azumi, T. (2016, October). Exploring the performance of ROS2. In Proceedings of the 13th international conference on embedded software (pp. 1-10).

## Slide 11: Components of ROS2
ROS2 is open source
The community
  Large community of users and developers contributing software packages
Computation graph
  ROS2 runs as a computational graph consisting of nodes and arcs
Workspace
  This is the user workspace that consists of the set of software installed on the robot or computer and the programs that the user develops

## Slide 12: The computational graph
Node: single purpose executable program
Topic: a named bus over which nodes exchange messages
Publication/subscription: nodes sending/receiving messages on a topic
Service: a synchronous request/response interaction between nodes: must be completed before the next one begins
Action: an asynchronous request/response interaction with feedback; can be performed concurrently without waiting for each other to complete
Source: Rico, F. M. (2022). A concise introduction to robot programming with ROS2. Chapman and Hall/CRC

## Slide 13: ROS2 workspace
Workspace directory
Source code of user programs (packages) are stored in src
  The workspace can contain multiple packages
  Each package is stored in 1 directory with CMakeList.txt and package.xml
Workspace needs to be built using colcon build
  build, install and log directories are created
To run the packages, the workspace needs to be sourced after building
  source install/setup.bash

## Slide 14: CMakeList.txt and package.xml
Must be placed at the root of the package directory
Defines the build tool, folders to be included, dependencies, etc

## Slide 15: Rviz2
Port of Rviz to ROS2
Installed by ROS2 by default
Provides graphic interface for users to view the robot, sensor data, maps, etc

## Slide 16: Gazebo
Open-source 3D robotics simulator developed and maintained by the Open Robotics Foundation
Commonly used together with ROS and ROS2
Features:
  Physics engines: e.g., ODE, Bullet, Simbody and DART
  3D graphics: uses Object-Oriented Graphics Rendering Engine
  Sensors and actuators: e.g., lidar, IMU, cameras, GPS, etc
  Plugins: easily extendable for custom functionalities
  World and environment: allows for complex and dynamic environments
  Multi-robot simulation
Gazebo classic and Gazebo (previously Ignition Gazebo)
We are using Gazebo Harmonic
Gazebo. Source: https://github.com/gazebosim
Gazebo Classic. Source: Rico, F. M. (2022). A concise introduction to robot programming with ROS2. Chapman and Hall/CRC

## Slide 17: ros_gz_bridge
A network bridge which enables the exchange of messages between ROS 2 and Gazebo Transport
We need a bridge because the robot is simulated in Gazebo, while the robot is controlled in ROS2; the messages of the robot from Gazebo must be ported to ROS2
Limited to only certain message types
There are several ways to configure the bridge; we will use a yaml file, which is the easiest way

## Slide 18: Marine Simulator Gazebo (marsim_gazebo) package
World
  Standard Gazebo physics, user commands, scene broadcaster, imu, sensors, dvl system and buoyancy plugins
  Seabed modelling using a heightmap model
  Custom-written Gauss Markov ocean current plugin
Cuurently only BlueROV2 model - main body with 6 thursters
  Buoyancy modelled using a rectangular collision geometry
  Standard Gazebo hydrodynamic, joint state publisher, pose publisher and odometry publisher plugins
  Thruster attached to main body using revolute joints with standard Gazebo thruster plugins
  Standard Gazebo IMU and DVL sensors with a custom-written ccp plugins and python scripts for post processing of measurements
  Simulated depth sensor using standard Gazebo odometry publisher with added noise using a custom-written python script
  ROS2 robot description and robot localization packages
  Custom-written python script for robot keyboard controller

## Slide 19: Custom-written plugins and scripts
Source codes are stored in /plugins and /scripts
marsim_gazebo::GaussMarkovOceanCurrent
marsim_gazebo::DVLRosConverter
depth_sensor_from_odom.py
noisy_odometry.py
ros_keyboard_controller.py
twist_stamper.py

## Slide 20: marsim1.1 ROS2/Gazebo model
Currently only the marsim_gazebo package
config: holds the configuration files such as the roz_gz_bridge yaml file
env-hooks: holds the files required to define paths
launch: holds the python launch files
models: holds folders which contain the models in sdf format
plugins: holds the cpp source codes (cc and hh files) for custom-made Gazebo plugins
rviz: holds the Rviz2 configuration yaml files
scripts: holds scripts that can be used to control the BlueROV2
worlds: holds sdf world files

## Slide 21: Starting up the model
ros2 launch marsim_gazebo empty_world.launch.py
ros2 launch marsim_gazebo spawn_bluerov2.launch.py
ros2 launch marsim_gazebo start_bridge.launch.py
ros run marsim_gazebo ros_keyboard_controller bluerov2

## Slide 22: ROS2-GZ bridge
We need a bridge because ROS2 and Gazebo are separate programs
Recap:
  ROS2 (Robot Operating System 2):
    A flexible framework for writing robot software
    Provides a collection of tools, libraries, and conventions for robot development
    Handles communication between different parts of a robotic system
    Supports multiple programming languages (C++, Python, etc.)
    Designed for distributed computing and real-time systems
    Used for both simulated and physical robots
  Gazebo:
    A 3D dynamic simulator for robots
    Provides accurate simulation of robots in complex indoor and outdoor environments
    Offers realistic sensor feedback and physically plausible interactions
    Can simulate multiple robots
    Often used in conjunction with ROS/ROS2 for testing and development

## Slide 23: ROS2-GZ bridge
Configured using bluerov2_ros_gz_bridge.yaml
Gazebo is the simulator, and ROS2 is the robot computer
Environment and robot measurements: Gazebo ---> ROS2
Robot commands: ROS2 ---> Gazebo

## Slide 24: rqt_graph
Namespace: bluerov2
Important nodes
  /ros_gz_bridge
  /ekf_filter
  /robot_state_publisher
  /depth_sensor_from_odom
  /noisy_odometry
  /twist_stamper
Important topics
  /bluerov2
  /tf
  /robot_description
  odometry
  odometry/filtered

## Slide 25: TF2 tree
No bluerov2/base_link/depth_sensor because the depth sensor is simulated using pose z measurements from /odometry with gaussian noise added

## Slide 26: EKF – Robot Localization package
Implemented using ROS2 robot localization package
Configured using bluerov2_ekf_config.yaml
imu0: standard Gazebo IMU sensor
  Orientations, angular velocities, linear accelerations
twist0
  Linear velocities
odom0
  Only pose z
Can be tuned through the defintion of the covariances

## Slide 27: EKF - Introduction
Purpose: State estimation for nonlinear systems
  Estimates the state of a dynamic system from noisy measurements
  Crucial for robotics, autonomous systems, and control applications
Extends the linear Kalman Filter to nonlinear systems
  Uses local linearization around the current state estimate
Key applications:
  Robot localization and navigation
  Sensor fusion in autonomous vehicles
  Spacecraft attitude determination
  Target tracking in radar systems
Addresses challenges of:
  System nonlinearity
  Measurement and process noise
  Multi-sensor integration

## Slide 28: EKF algorithm
The EKF algorithm aims to estimate the full 3D pose and velocity (6 pose states and 6 velocity states) of the robot over time
Consists of two steps: prediction and update
For more details, see Moore, T., & Stouch, D. (2016). A generalized extended kalman filter implementation for the robot operating system. In Intelligent Autonomous Systems 13: Proceedings of the 13th International Conference IAS-13 (pp. 335-348). Springer International Publishing.

## Slide 29: EKF algorithm – Robot state and measurements
Robot state: xk = f(xk-1) + wk-1
  xk is the 12-dimensional state vector (x, y, z, roll, pitch, yaw, vx, vy, vz, wx, wy, wz) at time k
  f is the nonlinear state transition function
  wk-1 is the process noise at time k-1 which is assumed to be normally distrubuted
Measurements: zk = h(xk) + vk
  zk is the measurement at time k
  h is the nonlinear sensor model that maps the states into the measurement space
  vk is the normally distributed sensor noise

## Slide 30: EKF algorithm – Prediction step
Project the current state estimate and error covariance forward in time:
State prediction: est(xk) = f(xk-1)
  est(xk) is the estimate of the state at time k
  f is robot model or nonlinear state transition function
  xk-1 is the state at time k-1
Covariance prediction: est(Pk) = FPk-1FT + Q
  est(Pk) is the estimated error covariance projected via F and perturbed by Q
  F is the Jacobian of f
  Q is the process noise covariance

## Slide 31: EKF algorithm – Correction step
Kalman gain calculation: K = est(Pk)HT(H est(Pk)HT + R)-1
  K is the Kalman gain
  H is the observation matrix, the Jacobian of h, the observation model function or the nonlinear sensor model. To support a wide array of sensors, H is an identity matrix in the robot_localization package.
  R is the measurement covariance
State update: xk = est(xk) + K(z – H est(xk))
Covariance update: Pk = (I - KH) est(Pk)(I – KH)T + KRKT

## Slide 32: EKF algorithm – Prediction step (more explanations)
State prediction: est(xk) = f(xk-1)
  This equation projects the state estimate forward in time
f represents the robot's motion model. For example, if the robot is moving at a certain velocity, f would use this information to predict where the robot will be at the next time step.
  The key point here is that f can be nonlinear, which is what distinguishes the Extended Kalman Filter from the regular Kalman Filter. This allows it to handle more complex systems and motions.

## Slide 33: EKF algorithm – Prediction step (more explanations) (2)
Covariance prediction: est(Pk) = FPk-1FT + Q
  F is the Jacobian of f and represents how changes in the previous state affect the current state. It's used to transform the previous covariance into the new time step. The use of the Jacobian F is another key aspect of the Extended Kalman Filter. It's a linear approximation of how the nonlinear function f behaves near the current estimate. This linearization is what allows the EKF to apply the Kalman Filter framework to nonlinear systems.
  FPk-1FT propagates the previous uncertainty through the state transition model.
  Q adds additional uncertainty due to imperfections in our model or external factors we can't account for.

## Slide 34: EKF algorithm – Correction step (more explanations)
Kalman gain calculation: K = est(Pk)HT(H est(Pk)HT + R)-1
  est(Pk)HT represents how much we expect the measurement to change based on changes in our state estimate
  H est(Pk)HT + R represents the total expected variance in our measurement (predicted measurement uncertainty + actual measurement noise).
  The inverse at the end turns this into a ratio - effectively, "how much should we trust this measurement compared to our prediction?
State update: xk = est(xk) + K(z – H est(xk))
  z – H est(xk)) is the difference between the actual measurement z and what we expected to measure K(z – H est(xk)). This is often called the "innovation" or "measurement residual".
  We multiply this difference by K to determine how much to adjust our prediction. If K is large, we adjust our estimate more towards the new measurement. If K is small, we trust our prediction more.

## Slide 35: EKF algorithm – Correction step (more explanations) (2)
Covariance update: Pk = (I - KH) est(Pk)(I – KH)T + KRKT
  I – KH represents how much of our previous uncertainty estimate we're keeping. If K is large (we trusted the measurement a lot), this term becomes smaller.
  est(Pk)(I – KH)T reduces our uncertainty based on how much information we gained from the measurement
  KRKT adds back some uncertainty based on how noisy our measurement was

## Slide 36
IMU + DVL + Depth sensors
IMU + DVL sensors
IMU sensor only
State estimations of position z when different combination of sensors are used
Measurements from the sensors:
IMU: ax, ay, az, ωx, ωy, ωz
DVL: vx, vy, vz
Depth: z
Huge drift in the state estimation due to accumulated error from the double time integration of az
A much smaller drift in the state estimation due to DVL sensor providing vz measurements which require only single time integration
The state estimation track readings of the depth sensor closely as it provides direct z measurements
Red line = estimated depth; Blue line = actual depth

## Slide 42
With camera and depth camera sensors

## Slide 43: Marine Simulator Control (marsim_control) package
Package where control-related source code will be placed
Common scripts where common functions are placed
  marsim_control/bluerov2_utils.py
  marsim_control/marsim_utils.py
scripts/bluerov2_pid_pose_z_control.py

## Slide 44: BlueROV2 thruster control configuration
For thruster control, the BlueROV2 has:
12 State vector components:
  Position (x, y, z)
  Orientation (roll, pitch, yaw)
  Linear velocity (vx, vy, vz)
  Angular velocity (ωx, ωy, ωz)
6 input vector components:
  Commands for 6 thrusters
z
x
y
T2
T1
T4
T3
x
y
T5
T6
Z-axis pointing out of the paper
Positive thrust for T5 and T6 is pointing upwards, i.e., pushes the ROV downwards

## Slide 45
PID depth control:
Going from –92 m to –90 m

## Slide 46: Planned updates for MARSIM v1.2
marsim_gazebo
  Add EKF with imu, dvl and depth sensors for models/sst
marsim_control
  Add displacement request and position hold for bluerov2 and sst

## Slide 47
Thank you for your attention!